## Slide 1
SHA-256 Accelerator on Zynq-7000
Measured results · verification · patent assessment
Amritha S · 23BEC1368 · ZedBoard XC7Z020-1CLG484 · Review 3, October 2026
Notes: Review 3. Results of the controlled 2x2 measurement, the verification stack, the toolchain, and the patent assessment.

## Slide 2
Design Space
One round module · five configurations · one constraint set
U = 1
U = 2
C = 1
C = 2
A
Iterative
66 cycles / block
B
2× unrolled
34 cycles / block
C
2-message interleaved
33 cycles / block (eff.)
D
Unrolled + interleaved
17 cycles / block (eff.)
B′ = B with h + K + W summed in parallel with the first round (operand-scheduled)
2

## Slide 3
Maximum Frequency on XC7Z020
Post-route · median of 5 placement seeds · Yosys + nextpnr-xilinx
Chart: Fmax (MHz)
| A | B | B′ | C | D
Fmax (MHz) | 68.24 | 45.92 | 44.41 | 68.2 | 40.18
0.673
Fmax(B) / Fmax(A)
0.999
Fmax(C) / Fmax(A)
0.651
Fmax(B′) / Fmax(A)
3
Notes: Absolute MHz come from the open-source timing model and are conservative; the ratios are the measurement. Seed ranges: A 64.5-70.5, B 44.5-48.2, B' 41.5-45.7, C 65.8-70.6, D 39.6-46.4.

## Slide 4
Pre-Registered Thresholds
Fixed at Review 1 · not moved
clears both
0.515 core break-even
0.624 system break-even
0.680 ngspice, scheduled
0.500 ngspice, serial chain
0.651 B′ measured
0.673 B measured
Unrolling is a net throughput gain on this device: 1.31× core, 1.08× system.
4
Notes: The pre-registered prediction was a net loss (ratio below 0.515). The measurement falsifies it on this flow; the thresholds themselves were not changed.

## Slide 5
Mechanism
Critical-path composition, post-route (seed 3)
Chart: 
| A | B
Logic (ns) | 3.7 | 4.8
Routing (ns) | 10.9 | 17
Carry-chain stages on path
A 10 · B 9
Logic delay, B vs A
+30 %, not +100 %
Synthesis of T1
adder tree, not serial chain
Hand-scheduled RTL (B′)
no gain · B′ ≡ B proven
5
Notes: The outcome of unrolling is decided by how synthesis structures the T1 adder, not by unroll depth and not by the operand order written in RTL.

## Slide 6
Transistor-Level Check
ngspice · Σ1 + N chained 32-bit adders · 180 nm LEVEL-1
Chart: adders in series
| 1 | 2 | 3 | 5 | 7 | 10
Simulated | 0.5506 | 0.8461 | 1.089 | 1.8387 | 2.4562 | 3.3595
Fit 0.2110 + 0.3169 N | 0.5279 | 0.8448 | 1.1617 | 1.7955 | 2.4293 | 3.38
R² = 0.998
delay linear in chain depth
0.500 → 0.680
B / A: serial vs scheduled
≤ 0.06 %
re-run deviation, 1 Oct 2026
6

## Slide 7
Throughput and Area
Core level at measured Fmax · system level with measured AXI cycles
Chart: 
| A | B | C | D
Core (Mbit/s) | 529.4 | 691.5 | 1058.1 | 1210.1
System (Mbit/s) | 411 | 443.6 | 684.7 | 587.8
 | LUT | FF | Mb/s/LUT
A | 1921 | 1035 | 0.276
B | 2298 | 1035 | 0.301
C | 3611 | 2059 | 0.293
D | 4486 | 2059 | 0.270
0 DSP · 0 BRAM in every configuration
Highest throughput: D, 2.29× A
Best per LUT: B
7

## Slide 8
Verification
Every layer runs in one command · all passing
129
RTL checks
Icarus Verilog
21
software checks
gcc
67
gate-level checks
Yosys netlist + Icarus
2
formal proofs, B′ ≡ B
Yosys SAT + induction
4 / 4
configs on virtual board
Verilator + unmodified main.c
0
A9 build warnings
arm-none-eabi-gcc -Werror
8
Notes: RTL: 103 checks for A-D plus 26 for B'. Gate-level: synthesised netlists of A, B, B', C, D under the unchanged RTL testbenches with Xilinx cell models. Formal: one round over all inputs, and the whole core over every state (4599 equivalence points). Virtual board: the bare-metal program runs against a Verilator model with real AXI4-Lite and AXI4-Stream transactions.

## Slide 9
Defects Identified and Corrected
Found by gate-level simulation and the virtual board
Area | Defect | Correction
Driver | Single-message hash stalled on dual-stream cores (C, D) | Lone message issued as a pair; one slot unused
Testbench | Stimulus applied at the clock edge (race) | Drive and sample 1 ns after the edge; 66 / 34 cycles confirmed
Firmware text | 112-byte NIST vector labelled 3 blocks | Corrected to 2 blocks
None of the three was visible to the original 103 RTL checks.
9

## Slide 10
Toolchain
Open-source verification flow · vendor flow for the board
Run in this project's cloud environment
Icarus Verilog 12
RTL and gate-level simulation
Verilator 5.020
virtual board (RTL + firmware)
Yosys 0.69
synthesis to LUT6 / CARRY4 · formal equivalence
nextpnr-xilinx + Project X-Ray
place, route, timing on XC7Z020
ngspice 42
transistor-level delay
arm-none-eabi-gcc 13.2
Cortex-A9 cross-compilation
Board flow (scripts ready)
AMD Vivado 2022.2
block design · bitstream · OOC Fmax
AMD Vitis 2022.2 (XSCT)
platform · application · JTAG
ZedBoard XC7Z020-1CLG484
target hardware
board/run_zedboard.sh A
10

## Slide 11
Hardware Realisation — ZedBoard
Vivado → Vitis → JTAG → UART
1
Vivado
PS7 + AXI DMA + accelerator
bitstream · XSA
2
Vitis
standalone platform
sha256_app.elf
3
JTAG
fpga · ps7_init
download · run
4
UART
115200 8N1
conformance report
Item | Status
Vivado system build, Vitis build, JTAG run scripts | ready
Expected UART transcript (virtual board, A–D) | recorded
Vivado OOC Fmax, on-board run, measured power | pending: Vivado host, ZedBoard
11

## Slide 12
Patent Assessment
Each candidate claim tested against prior art
Candidate claim | Prior art
Two-message interleaved core (C) | Helion 2010 (commercial IP) · IBM US20250070957A1 · SHARMONY, TCHES 2026
Unrolling with pipelining (D) | McEvoy, ISVLSI 2006 · Gamgam, ISCTürkiye 2023
Operand rescheduling of T1 | Chaves, CHES 2006 · Yao et al., Comput. J. 2025 · Intel SHA256RNDS2
Independence of the two axes | Leiserson & Saxe, Algorithmica 1991
Not patentable
no inventive step
Contribution
Controlled re-test of a published result, with a measured mechanism
12

## Slide 13
Position in the Literature
44 works reviewed · 2002–2026
44
works tracked
4
claims tested against prior art
1
published result re-tested
Published claim | This work, XC7Z020
Unfolding ×2 raises Fmax (Suhaili & Julai 2022) | does not reproduce — 0.673
Unfolding ×2 raises throughput (Suhaili & Julai 2022) | reproduces — 1.31×
Serial-chain model: Fmax halves | does not hold — synthesis builds a tree
Interleaving preserves Fmax (structural) | confirmed — 0.999
13

## Slide 14
Findings
0.673
Unrolling clears both pre-registered thresholds on XC7Z020.
Tree
Synthesis, not unroll depth or RTL operand order, decides the outcome.
0.999
Interleaving preserves Fmax; 2.00× throughput for independent messages.
Ready
Board flow scripted; Vivado Fmax and on-board run remain.