## Slide 1
FPGA-BASED SYSTEM DESIGN · PROJECT REVIEW 1
Unrolling Analysis of a
SHA-256 Hardware Accelerator
Does unrolling pay when the rounds are strictly sequential?
66 cycles vs 34 cycles · zero DSP48 · FIPS 180-4 verified
PRESENTED BY
Amritha S · 23BEC1368
TARGET DEVICE
ZedBoard · XC7Z020-1CLG484C
TOOLCHAIN
Vivado 2022.2 · Vitis 2022.2
DURATION
12 weeks
Notes: The project has a research question with a numeric threshold, stated before measurement. That is what lifts it above a plain implementation.

## Slide 2
Agenda
01
1
Problem Statement
Why hashes resist parallelisation
2
The Research Question
One inequality, stated before measuring
3
Literature Survey
Five clusters, 22 works reviewed
4
Positioning
A mature field — what I can honestly claim
5
Algorithm & Architecture
The round, and two ways to build it
6
Truth Tables & RTL
Exactly what goes into the fabric
7
Hardware & Software Spec
Device resources and toolchain
8
Verification, Timeline, Evaluation
FIPS 180-4 conformance
Review 1 · Amritha S · 23BEC1368 · 1

## Slide 3
Problem Statement
02
Stated first, before any solution is proposed
A block cipher in ECB mode unrolls and pipelines cleanly. A hash function cannot — and that constraint is the whole project.
P1
SHA-256 rounds are strictly data-dependent
Round t+1 consumes the working variables produced by round t. Two unrolled rounds cannot be separated by a pipeline register without forfeiting the cycle-count saving that motivated unrolling in the first place.
P2
Blocks chain through the hash value
Even across 512-bit blocks the chaining value carries forward, so a single message cannot be split across parallel engines. Only INDEPENDENT messages parallelise.
P3
The critical path is addition, and addition stacks
With rotations free and the logical functions shallow, the entire round delay is the five-input modulo-2³² sum forming T1. Unrolling puts two of those chains in series.
Review 1 · Amritha S · 23BEC1368 · 2

## Slide 4
The Research Question
03
One inequality — declared before the measurement is taken
Configuration B needs 1.94× fewer cycles per block.
Its maximum frequency will be lower. Is the product a net gain?
Fmax(B) / Fmax(A) > 34 / 66 = 0.515
above the threshold → unrolling is a net WIN · below it → a net LOSS, which is a valid and reportable finding
66
cycles per block
CONFIG A — MEASURED IN SIM
34
cycles per block
CONFIG B — MEASURED IN SIM
1.94×
fewer cycles
THE GAIN
0.515
frequency retention needed
THE BREAK-EVEN
Why stating the threshold in advance matters
Most implementation reports measure first and rationalise afterwards. Deriving the break-even condition from the cycle counts BEFORE synthesis turns this from a description into an experiment with a falsifiable prediction — and it means a negative result is still a result. Both configurations are built from the identical round module, so only unroll depth varies and the comparison is genuinely controlled.
Review 1 · Amritha S · 23BEC1368 · 3
Notes: If asked what happens when the result is a net loss: that IS the finding. It quantifies why hash functions parallelise badly within a single message.

## Slide 5
Objectives
04
Every objective has a pass/fail criterion, not a subjective one
ID | Objective | Measurable success criterion
O1 | Implement the six logical functions and the K constant ROM | Each matches the golden model; K ROM matches FIPS 180-4 §4.2.2
O2 | Implement the rolling sixteen-word message schedule | W[0..63] matches the golden schedule for a known block
O3 | Build Configuration A — iterative, one round per cycle | Correct digest for all NIST vectors; 66 cycles per block
O4 | Build Configuration B — two rounds per cycle | Bit-identical digest to Config A; 34 cycles per block
O5 | Integrate over AXI4-Lite and AXI4-Stream / DMA | Arbitrary-length message hashed correctly on hardware
O6 | Determine whether unrolling pays | Post-route Fmax and area for both; compared against 0.515
Definition of done: the ZedBoard hashes a message typed over UART and returns a digest matching the NIST reference, with both configurations synthesised under identical constraints and their frequencies compared against the stated threshold.
Review 1 · Amritha S · 23BEC1368 · 4

## Slide 6
Literature Survey I — Specification & Context
05
Cluster A: the authoritative ground truth this project verifies against
Source | Year | Contribution | Relevance to this project
NIST FIPS PUB 180-4 | 2015 | The Secure Hash Standard: padding §5.1.1, initial values §5.3.3, K constants §4.2.2, logical functions §4.1.2, compression §6.2.2 | PRIMARY REFERENCE. The whole verification strategy derives from it
NIST CAVP — Secure Hashing test vectors | — | Short-message, long-message and Monte Carlo vector sets | The long-message set exercises MULTI-BLOCK CHAINING, which single-block vectors do not
NIST SP 800-107 | 2012 | Security strengths and appropriate uses of approved hashes | Justifies SHA-256 specifically over SHA-1 or SHA-3
Wang, Yin & Yu — CRYPTO | 2005 | Theoretical collision attack on full SHA-1 | Why the field migrated to SHA-2
Stevens et al. — CRYPTO (SHAttered) | 2017 | The first practical SHA-1 collision | One motivational sentence: SHA-256 is necessary, not merely conventional
The K constants are "nothing up my sleeve" numbers — the fractional cube roots of the first 64 primes, derived by a publicly verifiable procedure so no hidden trapdoor can be alleged.
Review 1 · Amritha S · 23BEC1368 · 5

## Slide 7
Literature Survey II — Critical-Path Optimisation
06
Cluster B: every serious SHA-2 hardware paper is about shortening the adder chain
Work | Venue / Year | Contribution | How it bears on this project
Chaves, Kuzmanov, Sousa & Vassiliadis | CHES 2006 | OPERATION RESCHEDULING — precompute part of T1 one cycle ahead so the adder chain splits across the register boundary, shortening the path without changing the round count | THE most relevant paper. The obvious "how would you improve it" answer, and this project's documented future work
Dadda, Macchetti & Owen | DATE 2004 | Carry-save adder trees in the compression function | Confirms the five-input sum is the bottleneck; CSA is the standard remedy
McEvoy, Crowe, Murphy & Marnane | ISVLSI 2006 | FPGA-specific optimisation: pipeline the message schedule separately from the compression and balance the two | Supports the finding that the SCHEDULE unrolls for free while the COMPRESSION does not
Michail, Kakarountas, Milidonis & Goutis | IEEE TDSC 2009 | Systematic top-down methodology for unrolling and pipelining hash cores | Design-space taxonomy and terminology
Sklavos & Koufopavlou | ISCAS 2003 | Early comparative implementation across the SHA-2 family | Baseline area figures
Review 1 · Amritha S · 23BEC1368 · 6
Notes: Chaves 2006 is the paper to know. If asked how to shorten the critical path without unrolling, operation rescheduling is the answer.

## Slide 8
Literature Survey III — Why Hashes Resist Unrolling
07
Cluster C: the structural argument at the centre of this project
BLOCK CIPHER · AES-ECB
Blocks
INDEPENDENT of one another
Unrolled rounds
can be separated by registers
Combinational depth per stage
stays CONSTANT
Maximum frequency
PRESERVED
Throughput vs area
scales linearly
HASH FUNCTION · SHA-256
Rounds
round t+1 consumes round t
Unrolled rounds
a register would forfeit the saving
Combinational depth per stage
DOUBLES
Maximum frequency
MUST FALL
Throughput vs area
the question this project answers
One thing that DOES unroll for free: the message schedule. W[t+16] and W[t+17] both depend only on the current sixteen-word window, so the two schedule adders run in parallel with no serial dependency. Compression is the bottleneck; the schedule is not. Identifying exactly where the dependency lives is a substantive part of the analysis.
The right way to make a hash fast: multi-stream interleaving. Independent MESSAGES have no dependency, so N of them pipeline perfectly through an N-stage round unit — N× throughput for N× registers but the same round logic. This is what high-throughput hashing hardware does, and it is this project's documented future work.
Review 1 · Amritha S · 23BEC1368 · 7

## Slide 9
Positioning
08
SHA-256 hardware is a mature field — here is what I can honestly claim
SETTLED — NOT CLAIMED AS NOVEL
The five-input T1 addition is the critical path
Operation rescheduling and CSA shorten it
Schedule and compression optimise differently
The iterative 1-round-per-cycle baseline
WHAT THIS PROJECT CONTRIBUTES
1
A falsifiable prediction with a numeric threshold, stated BEFORE measuring
2
A controlled comparison — both configs share the identical round module
3
Hierarchical verification at eight levels, not end-to-end digest alone
4
Honest accounting of the modest software speedup, with the structural reason
Scope of the claim: the architectural options for SHA-2 were mapped between 2002 and 2009. I claim no new architecture and no record throughput. I claim a stated hypothesis, a controlled experiment, exhaustive verification and honest measurement on current silicon — a claim that survives questioning, which an inflated one would not.
Review 1 · Amritha S · 23BEC1368 · 8

## Slide 10
SHA-256 Compression Round
09
Sixty-four rounds — but six of the eight variable updates are free
T1 = h + Σ₁(e) + Ch(e,f,g) + K[t] + W[t] ← the critical path
T2 = Σ₀(a) + Maj(a,b,c)
h:=g g:=f f:=e e:=d+T1 d:=c c:=b b:=a a:=T1+T2
Ch, Maj
Bitwise choose and majority. Ch is a 2:1 mux with x as select; Maj is a 3-input majority gate.
1 LUT per bit
Σ₀, Σ₁, σ₀, σ₁
Three-input XOR of rewired copies of one operand. ROTR and SHR are fixed reorderings.
32 LUT each
T1 five-input add
Modulo-2³² sum of five 32-bit terms. This dominates the round delay entirely.
THE BOTTLENECK
Six renames
b:=a, c:=b, d:=c, f:=e, g:=f, h:=g are wire connections, not logic.
0 LUT
Why there are no DSP slices: SHA-256 contains no multiplication anywhere. Only 32-bit addition, XOR, AND, and fixed bit reorderings. With the rotations free and the logical functions one LUT deep, the entire cost of the design is addition — which is precisely why unrolling is expensive.
Review 1 · Amritha S · 23BEC1368 · 9

## Slide 11
Two Configurations, Identical Round Module
10
Only unroll depth and control differ — so the comparison is controlled
CONFIGURATION A
iterative — 1 round / cycle
Round instances
1, with feedback
Cycles per block
66 (1 load + 64 + 1 update)
Critical path
one 5-input adder chain
Throughput @ 100 MHz
≈ 776 Mbps
Projected core LUT
≈ 1,150
DSP48
0
CONFIGURATION B
2× unrolled — 2 rounds / cycle
Round instances
2, chained combinationally
Cycles per block
34 (1 load + 32 + 1 update)
Critical path
TWO chains in series
Throughput if Fmax held
≈ 1.51 Gbps
Projected core LUT
≈ 1,950
DSP48
0
The message schedule, by contrast, unrolls for free
w_new1 = σ₁(w[14]) + w[9] + σ₀(w[1]) + w[0] w_new2 = σ₁(w[15]) + w[10] + σ₀(w[2]) + w[1]
Both depend only on the CURRENT window contents, so the two schedule adders run in parallel with no serial dependency. Only the compression rounds stack — which is exactly where the frequency cost comes from.
Review 1 · Amritha S · 23BEC1368 · 10

## Slide 12
System Architecture
11
Complete PS-PL co-design — Vivado for the fabric, Vitis for the processor
PROCESSING SYSTEM (PS)
ARM Cortex-A9
667 MHz, bare-metal Vitis app
Message padding
FIPS 180-4 §5.1.1, in software
Block streaming
512-bit blocks → AXI DMA
Digest readback
256 bits over AXI4-Lite
NIST verification
compare against reference
Software SHA-256
baseline for speedup
UART report
digest + throughput, 115200
AXI4-Lite
ctrl + digest
AXI4-Stream
+ AXI DMA
AXI-HP
port
PROGRAMMABLE LOGIC (PL) — XC7Z020
AXI4-Lite Register File
init · start · status · digest[255:0]
AXI4-Stream Slave
512-bit block in, TLAST framing
MESSAGE SCHEDULE
rolling 16-word window · σ₀, σ₁ · 4-input add
COMPRESSION ROUND
Ch · Maj · Σ₀ · Σ₁ · T1 five-input add
CONFIG A: ×1 CONFIG B: ×2 chained
identical round module, different unroll
CHAINING VALUE H0..H7
8 × 32-bit accumulate, carries across blocks
Padding is performed by the PS, not the PL — a deliberate scope decision. Padding is byte-alignment bookkeeping; compression is the expensive part.
Review 1 · Amritha S · 23BEC1368 · 11

## Slide 13
Truth Table I — Ch and Maj
12
The two logical functions, exhaustively — one LUT per bit each
(a) Ch(x,y,z) = (x AND y) XOR (NOT x AND z)
x | y | z | Ch | Behaviour
0 | 0 | 0 | 0 | x=0 → select z
0 | 0 | 1 | 1 | x=0 → select z
0 | 1 | 0 | 0 | x=0 → select z
0 | 1 | 1 | 1 | x=0 → select z
1 | 0 | 0 | 0 | x=1 → select y
1 | 0 | 1 | 0 | x=1 → select y
1 | 1 | 0 | 1 | x=1 → select y
1 | 1 | 1 | 1 | x=1 → select y
(b) Maj(x,y,z) = (x·y) XOR (x·z) XOR (y·z)
x | y | z | Maj | Ones in
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 2
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 2
1 | 1 | 0 | 1 | 2
1 | 1 | 1 | 1 | 3
Ch is a multiplexer
Read the table by the x column: when x = 0 the output tracks z exactly; when x = 1 it tracks y.
Ch is therefore a bitwise 2:1 multiplexer with x as the select line — 32 multiplexers, one LUT each.
Maj is a majority gate
The output is 1 exactly when two or more inputs are 1 — visible in the rightmost column.
A 3-input function fits one 6-LUT with three inputs to spare, so Maj also costs 32 LUTs for the full word.
Review 1 · Amritha S · 23BEC1368 · 12

## Slide 14
Truth Table II — Why Rotation Costs Nothing
13
The bit mapping for Σ₀, showing it is routing rather than logic
Σ₀(x) = ROTR²(x) XOR ROTR¹³(x) XOR ROTR²²(x) out[i] = x[(i+2) mod 32] ⊕ x[(i+13) mod 32] ⊕ x[(i+22) mod 32]
Output bit | from ROTR² | from ROTR¹³ | from ROTR²² | Logic required
out[0] | x[2] | x[13] | x[22] | one 3-input XOR
out[1] | x[3] | x[14] | x[23] | one 3-input XOR
out[9] | x[11] | x[22] | x[31] | one 3-input XOR
out[10] | x[12] | x[23] | x[0] | one 3-input XOR ← wraps
out[31] | x[1] | x[12] | x[21] | one 3-input XOR
The consequence
Every source index is a COMPILE-TIME CONSTANT.
The rotation itself is wires — zero LUTs, zero flip-flops, zero delay.
The only logic in a whole Σ function is one 3-input XOR per bit:
32 LUTs for the entire 32-bit function.
SHR differs only in the shifted-in bits
Function | out[i] for i ≤ 28 | out[i] for i > 28 | Cost
ROTR³(x) | x[i+3] | x[i+3-32] wraps | routing
SHR³(x) | x[i+3] | hard 0 | routing
Where the cost actually is
With rotations free and Ch, Maj, Σ all one LUT deep, the entire round delay is the five-input modulo-2³² addition forming T1.
That is why unrolling costs frequency.
Review 1 · Amritha S · 23BEC1368 · 13

## Slide 15
Truth Table III — Control FSM & Message Schedule
14
Sequencing the core, and the rolling window that saves 1536 bits
(a) Control FSM state transition table
Present state | Condition | Next state | Action
IDLE | block_valid | ROUND | load W[0..15]; a..h ← H (or H(0) if init)
ROUND | t < 63 (A) / t < 62 (B) | ROUND | execute round(s); advance schedule window
ROUND | t = 63 (A) / t = 62 (B) | FINAL | last round complete
FINAL | — | IDLE | H += a..h; assert digest_valid
(b) The rolling sixteen-word message schedule
Window slot | Holds | Used for | Why kept
w[0] | W[t] | the current round, and the recurrence | W[t-16] term
w[1] | W[t+1] | σ₀ input | W[t-15] term
w[9] | W[t+9] | direct addend | W[t-7] term
w[14] | W[t+14] | σ₁ input | W[t-2] term
w[15] | W[t+15] | receives the newly computed word | newest entry
Sixteen words, not sixty-four
W[t] reaches back at most sixteen words, so a 16-deep shift register is sufficient.
Storing the full expanded schedule would cost 2048 bits instead of 512 — 1536 bits wasted for no functional benefit.
w_new = σ₁(w[14]) + w[9] + σ₀(w[1]) + w[0] then shift down by one and load w_new into w[15]. Config B computes two new words per cycle and shifts by two.
Review 1 · Amritha S · 23BEC1368 · 14

## Slide 16
Exactly What Gets Implemented
15
RTL module hierarchy — written, simulated and passing
Module | Level | Function | Est. resource
sha256_ch.v | L0 | Bitwise choose — 2:1 mux per bit | 32 LUT
sha256_maj.v | L0 | Bitwise majority | 32 LUT
sha256_big_sigma0/1.v | L0 | 3-input XOR of rewired copies | 32 LUT each
sha256_small_sigma0/1.v | L0 | As above, with SHR instead of one ROTR | 32 LUT each
sha256_k_rom.v | L0 | 64 × 32-bit round constants | ~200 LUT
sha256_round_comb.v | L1 | One full round: T1, T2, variable update | ~450 LUT
sha256_core_iter.v | L2 | CONFIG A — 1 round/cycle, 66 cycles | ~1,150 LUT
sha256_core_unroll2.v | L2 | CONFIG B — 2 rounds/cycle, 34 cycles | ~1,950 LUT
axi_lite_regs.v | L3 | control, status, digest readback | ~450 LUT
axis_wrapper.v | L3 | AXI4-Stream slave, 512-bit blocks | ~300 LUT
sha256_top.v | L4 | Top-level IP for Vivado IP Integrator | —
Device budget
Config A total
~3,700 (7%)
Config B total
~4,500 (8%)
BRAM
0 of 140
DSP48E1
0 of 220
21 / 21
verification checks passing
in simulation today
Both cores already produce the correct NIST digests, including multi-block chaining.
Review 1 · Amritha S · 23BEC1368 · 15

## Slide 17
Verification Strategy
16
Hierarchical conformance against FIPS 180-4, not end-to-end digest alone
Level | What is checked | Verified against | Status
Σ₀, Σ₁, σ₀, σ₁ | Known values on a fixed operand | Python golden model | PASSING
Ch, Maj | Selector and majority behaviour | Truth tables, slide 12 | PASSING
K constant ROM | Boundary entries K[0], K[15], K[32], K[63] | FIPS 180-4 §4.2.2 | PASSING
Message schedule | W[0..63] for a known block | Golden schedule file | file ready, TODO
Per-round a..h | All 64 rounds of working variables | Golden trace file | file ready, TODO
Single-block digest | "abc" and the empty message | NIST vectors | PASSING
Multi-block chaining | 56-byte message spanning two blocks | NIST vector | PASSING
Config A vs Config B | Bit-identical digest | Each other | PASSING
Cycle counts | 66 and 34 per block | Design intent | PASSING
Why hierarchy matters here
Hash bugs — a big-endian word swap, a schedule off-by-one, a missing final accumulation — all produce output that looks like a valid digest. End-to-end testing cannot localise them; per-round traces can.
The self-check needing no reference
Configurations A and B share the identical round module but differ in control and unroll depth. Requiring bit-identical digests from both is an independent check — a control-path error in either breaks the match immediately.
Review 1 · Amritha S · 23BEC1368 · 16

## Slide 18
Hardware Specification
17
ZedBoard · Zynq-7000 XC7Z020-1CLG484C
PROGRAMMABLE LOGIC (PL)
Fabric
Artix-7 equivalent, 28 nm
Logic cells
85,000
6-input LUTs
53,200 (A ≈ 7%, B ≈ 8%)
Flip-flops
106,400
Block RAM
140 × 36 Kb (using 0)
DSP48E1 slices
220 (using 0)
PL clock
100 MHz oscillator
PROCESSING SYSTEM (PS)
Processor
Dual-core ARM Cortex-A9
Frequency
667 MHz
External memory
512 MB DDR3
Boot / storage
256 Mb QSPI flash, SD card
PS reference clock
33.333 MHz
PS-PL interfaces
4 × AXI-HP, 2 × AXI-GP, ACP
Console
USB-UART, 115200 8N1
Why this is a frequency study, not an area study
Both configurations occupy under 10% of the device and use no BRAM and no DSP. Area is simply not the binding constraint here — which is precisely what makes the unrolling question interesting. The trade is cycles against frequency, and the device has ample room for either answer. Whether the K constants live in LUT ROM (current) or BRAM is a secondary experiment worth measuring but not decisive.
Review 1 · Amritha S · 23BEC1368 · 17

## Slide 19
Software Specification & Toolchain
18
Both mandated tools are load-bearing — Vivado for the fabric, Vitis for the processor
Vivado 2022.2
RTL synthesis and implementation, both configurations
IP Integrator block design (ZYNQ7 PS, AXI DMA)
Timing closure and utilisation per configuration
THE Fmax comparison that answers the research question
Waveform capture for the report
Vitis 2022.2
Bare-metal C application on Cortex-A9
FIPS 180-4 message padding in software
AXI DMA driver (xaxidma), BSP generation
ARM global timer for throughput measurement
Software SHA-256 baseline and NIST verification
Verification & modelling
Icarus Verilog / ModelSim — RTL testbenches
Python 3 — SHA-256 reference model
NIST FIPS 180-4 and CAVP test vectors
Per-round trace and schedule files as testbench input
Reference model built BEFORE any RTL
Languages
Verilog HDL
All RTL — functions, schedule, both cores, AXI
C (bare-metal)
PS app, padding, DMA driver, verification, UART
Python 3
Golden model, vector and trace generation
Tcl
Vivado build automation for both configurations
Review 1 · Amritha S · 23BEC1368 · 18

## Slide 20
12-Week Plan
19
Config A demonstrable by Week 9; Config B is the experiment
1
Python reference; K constants, vectors, per-round trace
Model passes all five FIPS 180-4 vectors
2
Logical functions and K ROM in Verilog
Each verified against the model
3
Rolling sixteen-word message schedule
W[0..63] matches the golden schedule
4
sha256_round_comb + Config A FSM
Round matches the golden trace
5
Config A full hash
Correct digest, single and multi-block
6
BUFFER WEEK
slack — no scheduled deliverable
7
AXI4-Lite + AXI4-Stream wrappers, IP packaging
AXI protocol checks clean
8
Block design, DMA, Config A implementation
Timing closed; area and Fmax recorded
9
Vitis application; on-board verification
Hardware digest matches NIST
10
Config B; implementation; THE Fmax comparison
Break-even evaluated against 0.515
11
Software baseline; throughput; report drafting
All measurement data collected
12
Waveforms, demo, final submission
Deliverables complete
Config B is scheduled at Week 10, after Config A works on hardware. A schedule slip degrades the project to a complete verified single-configuration deliverable, not a failure.
Review 1 · Amritha S · 23BEC1368 · 19

## Slide 21
Evaluation Metrics & Expected Outcomes
20
Nine measurements, each against a named baseline
Metric | Measurement method | Baseline | Target / expectation
Functional correctness | NIST vectors, hierarchical | FIPS 180-4 | Exact match
Cross-validation | Bit-identical digest | Config A vs B | Exact match
Cycles per block | Simulation counter | Design intent | 66 and 34 (confirmed)
Maximum frequency | Post-route, identical constraints | Config A vs B | Measured
Fmax ratio vs 0.515 | Derived | Break-even threshold | THE HEADLINE RESULT
Net throughput | Cycles × frequency | Each other | Measured
LUT / FF / BRAM | Post-implementation report | Each configuration | A ≈ 7%, B ≈ 8%
DSP48E1 usage | Utilisation report | — | Exactly 0
Speedup over software | ARM global timer | Cortex-A9 software SHA-256 | ≈ 3× (see note)
On the modest software speedup — do not hide it, explain it
SHA-256 is built from 32-bit addition, XOR and rotation — precisely the operations a general-purpose ALU executes in one cycle each. Unlike a block cipher, whose finite-field arithmetic a processor must emulate, there is nothing here the CPU is bad at. A ~3× speedup is expected and correct. The value of a SHA-256 accelerator is offload and deterministic latency, not raw throughput multiplication.
Review 1 · Amritha S · 23BEC1368 · 20

## Slide 22
Scope Boundaries & Risk Register
21
What is excluded, why — and what could go wrong
Explicitly out of scope
Hardware message padding
Byte-alignment bookkeeping; the PS does it. Future work.
SHA-224 / 384 / 512
224 is an IV change; 384/512 need a 64-bit datapath and 80 rounds
HMAC-SHA256
Two nested hashes plus key padding — a wrapper, not a modification
4-way multi-stream interleaving
The RIGHT way to get real hash throughput. Documented as the natural next step.
Side-channel resistance
Separate research field
Risk register
R1
Big-endian word ordering
High
The classic hash bug. Golden model emits blocks in the exact expected order
R2
Schedule window off-by-one
High
Golden schedule file compared word by word, not only at the digest
R3
Missing final H accumulation
Med
Caught immediately by the "abc" vector
R4
Config B fails timing badly
Med
THIS IS THE RESULT, not a failure — it answers the question
R5
Chaining not carried across blocks
Med
Explicitly tested by the 56-byte two-block NIST vector
R4 deserves emphasis: if Configuration B loses more frequency than it saves in cycles, that is not a failed implementation — it is a quantified answer to the research question, and it explains why hash functions parallelise badly within a single message. The report is written to accommodate either outcome.
Review 1 · Amritha S · 23BEC1368 · 21

## Slide 23
Key References
22
Selected from 22 works reviewed across five clusters
[1] NIST, "Secure Hash Standard (SHS)," FIPS PUB 180-4, August 2015.
[2] NIST, Cryptographic Algorithm Validation Program — Secure Hashing test vectors.
[3] NIST, "Recommendation for Applications Using Approved Hash Algorithms," SP 800-107.
[4] X. Wang, Y. L. Yin and H. Yu, "Finding Collisions in the Full SHA-1," CRYPTO, 2005.
[5] M. Stevens et al., "The First Collision for Full SHA-1," CRYPTO, 2017.
[6] R. Chaves, G. Kuzmanov, L. Sousa and S. Vassiliadis, "Improving SHA-2 Hardware Implementations," CHES, 2006.
[7] L. Dadda, M. Macchetti and J. Owen, "The Design of a High Speed ASIC Unit for the Hash Function SHA-256," DATE, 2004.
[8] R. P. McEvoy, F. M. Crowe, C. C. Murphy and W. P. Marnane, "Optimisation of the SHA-2 Family of Hash Functions on FPGAs," ISVLSI, 2006.
[9] H. Michail, A. P. Kakarountas, A. Milidonis and C. E. Goutis, "A Top-Down Design Methodology for Ultrahigh-Performance Hashing Cores," IEEE TDSC, 2009.
[10] K. K. Ting, S. C. L. Yuen, K.-H. Lee and P. H. W. Leong, "An FPGA Based SHA-256 Processor," FPL, 2002.
[11] N. Sklavos and O. Koufopavlou, "On the Hardware Implementations of the SHA-2 Hash Functions," ISCAS, 2003.
[12] ARM, AMBA AXI and ACE Protocol Specification, IHI 0022.
[13] Xilinx, AXI DMA Product Guide (PG021); Zynq-7000 TRM (UG585); Vivado Synthesis (UG901).
Review 1 · Amritha S · 23BEC1368 · 22
Notes: VERIFY EVERY CITATION before the review. FIPS 180-4 is certain; the conference papers need year and venue confirmed on IEEE Xplore or IACR ePrint.

## Slide 24
In one sentence
Build SHA-256 in fabric two ways from the same round module, verify both exactly against the NIST vectors, and measure whether unrolling a strictly sequential hash is worth what it costs in frequency.
Confirmation
Is the scope right for the weighting?
Board access
ZedBoard availability, Weeks 8-12
Config B
Required, or acceptable as upside?
Thank you — questions welcome
Amritha S · 23BEC1368 · amritha.s2023@vitstudent.ac.in