## Slide 1
The Design Space
04
Unrolling is one lever. Interleaving is a second, independent one. This project measures both.
U = 1 one round per stage
U = 2 two rounds per stage
C = 1
one message
C = 2
two messages
A
BASELINE
66 cycles / block
critical path: 1 round
B
UNROLLED
34 cycles / block
critical path: 2 rounds
C
INTERLEAVED
33 cycles / block
critical path: 1 round
D
BOTH LEVERS
17 cycles / block
critical path: 2 rounds
One round module, four configurations
The number of round instances and the placement of registers are the only variables between them.
Notes: U is unroll depth, C is interleave depth. C and D hash two independent messages at once, so their per-block cost is the effective figure: 66 cycles retiring two blocks is 33 per block. Cycle counts are confirmed in simulation, not estimated.

## Slide 2
Two Levers, Two Bargains
05
Moving across the grid and moving down it are not the same trade.
ACROSS A ROW — UNROLLING
Buys cycles, pays frequency
Two rounds chained combinationally put two five-input adder chains in series. The critical path doubles, so the clock must slow. Whether the cycle saving outweighs it is a real question.
May lose. Break-even at 0.624.
DOWN A COLUMN — INTERLEAVING
Buys cycles, pays area
A register between the round instances is legal because the two messages are independent. The critical path is unchanged, so no frequency is traded. The cost is a second set of registers.
Cannot lose, absent a build error.
The prediction
Because the interleave register never touches the combinational path, the gain down a column should not depend on which column it is: A→C and B→D should both be close to 2×, whatever unrolling does. That independence is the claim the measurement tests.
Notes: 0.624 is the system-level break-even: Config B wins only if it keeps more than 62.4% of Config A's frequency. It was derived from cycle counts and committed before synthesis. It can still fail, and that remains a valid reportable outcome.

## Slide 3
Novelty and Contribution
06
The contribution is a controlled re-test of a published result that contradicts theory.
01
A re-test of a contradictory result
Suhaili & Julai (2022) report the same 64-to-34-cycle design improving Fmax, against theory and the classical literature. Their designs were built separately, so architecture, device and toolchain cannot be told apart.
02
A controlled 2×2 measurement
Four cores, one round module, one script, one constraint set, one device. It also tests whether the interleave gain stays independent of unroll depth on real fabric, as C-slow retiming theory predicts.
03
A threshold that can still fail
Config B's break-even was fixed before synthesis and may be missed. Adding C and D gives a positive result without softening that.
No novelty is claimed in unrolling, interleaving or pipelining. All three are published, and the independence of the two axes follows from C-slow retiming theory. What is new is the controlled re-test.
Notes: This slide replaces the Review 1 novelty slide. That one offered experimental method as the contribution and conceded a negative result was possible. This one offers a structural claim about the design space and keeps the falsifiable threshold intact.

## Slide 4
What the Literature Says
07
A 2022 result contradicts the structural theory. That is the gap.
SUHAILI & JULAI, 2022 · ARRIA II GX
Unrolling improved Fmax
Builds the same unfolding-by-two design, 64 rounds in 34 cycles, and reports that it surpassed the iterative design on maximum frequency.
THE STRUCTURAL ARGUMENT
Fmax must fall
Two adder chains in series cannot be separated by a register without losing the cycle saving. The critical path doubles, so the clock slows.
Why it is still open
Their three designs were built separately, so a frequency difference cannot be attributed to unroll depth rather than to the device or the toolchain.
Arria II GX is not Zynq-7020. Whether a second adder chain fits the timing budget is a device question. An Altera answer does not transfer to Xilinx fabric.
The field is active, not settled. Two 2026 papers place SHA-256 on Zynq-7000, one on the ZedBoard itself.
Notes: This is the honest answer to 'hasn't this been done'. Yes, and the published answers disagree with each other and with theory. Our construction removes the confound: identical round module, identical constraints, one device.

## Slide 5
Verification Status
08
69 RTL checks and 10 software checks, all passing.
69
RTL checks
10
software checks
64
rounds traced
0
failures
What is checked
Logical functions and K ROM against the Python model
Message schedule W[0..63] at all 64 rounds
Per-round a..h at all 64 rounds
NIST vectors including multi-block chaining
Soak: 12 messages at 55, 56, 63, 64 and 65 bytes — the padding boundaries that break most designs
Four-way agreement: A, B and both streams of C and D must produce bit-identical digests
Cycle counts 66, 34, 33 and 17 confirmed in simulation
Notes: The four-way agreement check is the strongest one: it needs no external reference. The four cores share a round module but differ in control, so any control-path error breaks the match immediately.

## Slide 6
The Measurement
09
Four out-of-context builds, one script, one constraint set.
Why the timing constraint is deliberately unreachable
Vivado stops optimising once timing is met, so at 100 MHz all four would meet it with slack and the result would record where the tool chose to stop. The target is set at 250 MHz instead, pushing every configuration to its own limit under the same pressure. Negative slack is the measurement, not a failure.
Config B clears 0.624
Unrolling pays. Report the gain and the ratio.
Config B misses 0.624
A net loss on this device — the stated falsifiable outcome, and a valid finding.
A→C and B→D agree
The two axes are independent. The orthogonality claim is confirmed.
Every outcome is reportable. The project does not depend on any one of them landing a particular way.
Notes: Throughput-per-LUT is the headline metric because the four configurations differ in area. State the caveat out loud: C and D need independent messages, and single-message latency is unchanged.